## Slide 1
KNOWLEDGE BASED SYSTEMS / CT-359
Robotic Arm
Fault Diagnosis
Explainable rule engine · source-aware evidence · maintenance workflow
Semester project | Saad Ali · 24221 | NED University
Notes: Project framing and supplied assignment: Knowledge Based Systems CT-359 CCP brief, NED University, 2026.

## Slide 2
KBS CT-359 / ARM INSIGHT
Problem and scope
02
A protective stop can have several plausible causes. An operator needs to see why a hypothesis appeared and what observation is still missing.
Input: manual observations or source-tagged claims
Output: supported, possible, contradicted or conflicted hypotheses
Boundary: academic screening on a generic arm; no automated control

## Slide 3
KBS CT-359 / ARM INSIGHT
Knowledge representation
03
SYMBOLS
SYMPTOMS
RULES
yes · no
unknown · conflict
A structured JSON dictionary links observations with component and fault context.
Eight fault frames contain required conditions, causes and qualified actions.
The knowledge base stays inspectable and editable for demonstration.

## Slide 4
KBS CT-359 / ARM INSIGHT
Forward-chaining diagnosis
04
Observed facts
Rule match
Explanation
Protective stop = Yes
Payload mismatch = Yes
Payload condition group is satisfied. The rule derives a fault hypothesis.
The trace lists satisfied facts and suggests a qualified payload check.
Unknown leaves a rule possible. No contradicts it. Conflict blocks support.
Notes: Illustrative reasoning. Universal Robots C162 documentation discusses incorrect payload center of gravity as a possible cause of protective stop: https://www.universal-robots.com/manuals/EN/HTML/SW5_19/Content/prod-err-codes/topics/CODE_162.html . The app is generic and its rule is not model-specific validation.

## Slide 5
KBS CT-359 / ARM INSIGHT
Conflicting observations
05
Operator observation
Protective stop = Yes
Sensor / controller
Protective stop = No
Resolved state: CONFLICT
The system preserves both source records and marks affected rules conflicted. A technician can review the evidence and enter a qualified follow-up.

## Slide 6
KBS CT-359 / ARM INSIGHT
Web app workflow
06
Capture symptoms and evidence sources
Review hypotheses, missing inputs and rule trace
Save cases, compare investigations and track maintenance tasks
Export a case report or run the evaluation suite
Runs locally through a small static-file server. Case data stays in browser storage.

## Slide 7
KBS CT-359 / ARM INSIGHT
Dataset and verification
07
13
synthetic scenarios
8
inference checks
9
storage validation checks
Plus 7 evidence tests for source-claim validation and conflict resolution.
Notes: Counts are executable local regression checks, not an estimate of diagnostic accuracy. Test commands and scenarios are included in the source package.

## Slide 8
KBS CT-359 / ARM INSIGHT
Evaluation and limitations
08
Why forward chaining?
The task screens across multiple faults from entered observations, while exposing each rule match in a trace.
What remains unverified?
No live telemetry, field-labelled cases, model-specific thresholds or expert validation. Source labels do not authenticate claims.
A qualified engineer must approve any real maintenance action.
Notes: The cited UR references support selected protective-stop examples, not the complete generic rule base: https://www.universal-robots.com/articles/ur/robot-care-maintenance/understanding-protective-stops/ and https://www.universal-robots.com/manuals/EN/PDF/SW5_24/service-manual_e-series/e-Series_Service_Manual_en.pdf

## Slide 9
KBS CT-359 / ARM INSIGHT
Five-minute viva demonstration
09
1 Load the payload scenario and open the rule trace
2 Save the case and compare it with another investigation
3 Add opposing source claims to show conflict
4 Create a maintenance task and run the test suite
Close with the scope: transparent software behavior on synthetic data.